## Slide 1
Kubernetes Persistence

## Slide 2: What‘s the issue?
Pods are ephemeral and can vanish any moment
Data residing in a pod will vanish with the pod
Pod-A
IP: 10.10.10.1
volume
container
nginx
Notes: Pods provide only ephemeral storage. When a pod is killed, all data is gone. This section is all about the creation & usage of storage in the context of Kubernetes.

## Slide 3: How to solve it?
Pod-A
IP: 10.10.10.1
Storage backend
Container:
mount as /mnt/
Let the pod access persistent storage
Kubernetes offers different types of storage integration:
  https://kubernetes.io/docs/concepts/storage/volumes/
reference
Notes: Add the reference to the storage to the pod definition in spec.volumes
Refer to the spec.volumes entries in the container spec and define to which location the bind-mount should point. If the container places data at /mnt/, it will be persisted on the actual storage

## Slide 4: Volumes & VolumeMounts
Volumes are part of the PodSpec object
Provide direct access to storage
Available for a lot of backends
  local storage (nfs, hostPath, ceph)
  cloud storage (Azure, GCP, AWS,…)
Make storage available in a container via VolumeMounts as part of the container specification
Special volumes:
  emptyDir
  secret
  configMap
Notes: To use persistent storage within a container, firstly you need to make it available to the pod. This is done by specifying a volume object on PodSpec level. A volume could link to a NFS share, some local storage cluster like ceph or glusterfs or even access the storage provided by cloud platforms like GCP, AWS or Azure. It is also possible to share storage that is part of a cluster node itself (hostPath). However this is quite dangerous as you need to ensure this storage is available (incl. content) on every single cluster node.
In addition there are other special volume types:
emptyDir: temporary storage, usually to cache or test something. Its lifecycle is bound to the pod and therefore data is ephemeral as well
Secret & configMaps: hold confidential or configuration data and are accessed also via the volumes interface.

## Slide 5: Are there drawbacks of direct storage integration?
Notes: Drawbacks:
Maintain credentials to access storage within the pod
Have dependencies to infrastructure already at pod level
Hard to manage data lifecycle
Does it scale with the number of pods?
There are several ways of adding storage. Of course you can attach storage directly as a so called volume. However there might be drawbacks doing so. Hence we introduce a different way involving another abstraction layer.

## Slide 6: Storage with PersistentVolumes & PersistentVolumeClaims
Administrator space
Physical storage
Pod-A
container
nginx
Persistent Volume
Persistent Volume Claim
User space
Persistent Volumes objects represent physical storage
Create a Persistent Volume Claim to bind the Persistent Volume
Use the claim as a volume in a pod.
Note: the claim has a separate lifecycle.
Notes: Managing storage is a distinct problem from managing compute. The PersistentVolume subsystem provides an API for users and administrators that abstracts details of how storage is provided from how it is consumed. To do this we introduce two new API resources: PersistentVolume and PersistentVolumeClaim.
A PersistentVolume (PV) is a piece of storage in the cluster that has been provisioned by an administrator. It is a resource in the cluster just like a node is a cluster resource. PVs are volume plugins like Volumes, but have a lifecycle independent of any individual pod that uses the PV. This API object captures the details of the implementation of the storage, be that NFS, iSCSI, or a cloud-provider-specific storage system.
A PersistentVolumeClaim (PVC) is a request for storage by a user. It is similar to a pod. Pods consume node resources and PVCs consume PV resources. Pods can request specific levels of resources (CPU and Memory). Claims can request specific size and access modes (e.g., can be mounted once read/write or many times read-only).

## Slide 7: Storage with PersistentVolumes & PersistentVolumeClaims
PV:PVC is always 1:1
PV size must match or exceed PVC requested size
PVC is used as volume within the pod
Notes: 1 PV is always bound by exactly 1 PVC. There is no real order but Kubernetes tries to create matches between requested and provisioned size.
Problem: the match making is based on “equals or greater”. So if the PVC requests 1GB but there is only one PVC with 50GB available, it will be bound nevertheless (and “waste” 49GB)

## Slide 8: PV/PVC lifecycle
Persistent Volume
Persistent Volume Claim
Deleting a PVC could cause the following:
Retain – PV still exists including all data
Delete – delete the PV and all data
Recycle – delete data and make PV available again to be bound by a different PVC
Notes: Upon deletion of the claim object the persistent volume becomes “unbound”.
There are 3 scenarios:
Retain: nothing happens, the PV will remain until an administrator deals with it. The data is not (yet) deleted.
Delete: together with the PVC also the PV will be deleted. All data is gone.
Recycle (deprecated): remove all data and make PV available to be bound again by a different PVC

## Slide 9: Access Modes
Persistent Volume Claim
Pod A2
Pod A3
Pod A1
IP: 10.10.10.1
IP: 10.10.10.2
IP: 10.10.10.3
Physical storage
Persistent Volume
RWO = read-write once
Only 1 pod can mount the PVC
ROX = read-only many
Multiple pods can mount read-only or 1 pod read-write
RWX = read-write many
Multiple pods can mount read-write
Storage backend has to support access modes
Notes: Modes depend on the storage backend (physical storage). Example for RWX is NFS

## Slide 10: Storage Classes
Provisions a PV for based on PVC request
Overcomes need to manually provision PV (which is not namespaced and could be claimed by anybody)
Notes: Due to the PV-PVC bind mechanism, it might happen that storage is claimed by the “wrong” requests. Storage classes overcome this issue by reversing the order. Firstly create a PVC and the storage class provides a fitting PV.
On Kubernetes level a storage class is a piece of software running inside the cluster that also is able to administer the storage backend.

## Slide 11: Demo
Show existing PV & PVC
Show storage class
Create a PVC and display status
Show corresponding PV

## Slide 12: What YOU will do during the next exercise…
nginx
nginx
nginx
content
config
tls certs